## Slide 1: Data Process & Noise Subtraction
谢芳

## Slide 2: Data Process Work Flow
DAQ
Convert Data Format
Derivative Trigger
Noise Subtraction Module
Pulse Shape Cut
Optimal Filter
Extract Amplitude
Spectrum,
etc.

## Slide 3: Derivative Trigger (DT)
Set DT flag, record the event within 10s window
Continues Derivative > 0
Threshold > 3 times RMS
Baseline slope projected to X-axis
Use 3s before trigger to calculate baseline RMS.

## Slide 4: Triggered Examples

## Slide 5: Triggered Examples
Project to the X-axis and calculate baseline RMS
Trigger algorithm developed using python3

## Slide 6: Noise Subtraction Principle
Δt=0
Δt=t’
reference
Δt=tbest
shift baseline
C++ based algorithm developed by Shihong Fu
re-written as plug-in module based on python3 by Fang

## Slide 7: Noise Subtraction
An example implemented on CUORE data
Unfortunately, due to high background event frequency and less stable baseline during the test runs at USTC and Fudan, it is hard to implement this method at the moment.
V′ (t0) = V(t0) − V(t0 − Δt)

## Slide 8: Pulse Shape Cut
preliminary scheme: cut on the pulse width
Consider to add more precise parameters: raise time, decay time, etc

## Slide 9: Obtain the Spectrum
Preliminary result
Preliminary result
With calibration source 22Na
Without calibration source 22Na
Data from USTC LMO test run13 with water shielding,
sample rate 0.001s, ~4 day run each, with & without 22Na
Need to understand the the second major peak, it is too wide.

## Slide 10: To Do: Optional Modules & Denoise
Upgrade the pulse cut
Optimal Filter Module
Re-trigger Module: optimize the trigger algorithm. For example, for the baseline slope, do liner fit to find the
kx+b